## Slide 1: XFLR5 Methods and Their Application in “Constraints on the Wing Morphology of Pterosaurs”
By: Colin Parker

## Slide 2: Constraints on the wing morphology of pterosaurs
Wing shape is a mystery
  Few soft tissue fossils
No studies looking at the aerodynamic components
Want to combine biomechanical and aerodynamic constraints to predict shape

## Slide 3: Longitudinal Stability Analysis

## Slide 4: Effects of Washout

## Slide 5: XFLR5

## Slide 6: Python Coding
Create dictionary that includes each wings class
Allows the calling of a specific wing class without storing different variables

## Slide 7: LLT Lifting Line Theory
Kutta_Joukowski
Biot-Savart
Helmholtz Theorem
  The strength of a vortex filament is constant along its length
  A vortex filament cannot end in a fluid: must extend to infinity or form a closed path
Effective angle of attack
Repeat

## Slide 8: LLT
Limitations
Does not account for sweep
Does not account for dihedral
Inviscid
Must have high Aspect Ratio

## Slide 9: Lifting Surface Theory
Series of lifting lines
Circulation varies in both
  Span wise lifting line
  Chord wise vortices
Chord wise vortices extend into wake.
Biot-Savart
Flow tangency condition

## Slide 10: VLM Vortex Lattice Method
Assign circulation at control points
Biot-Savart Law
Flow tangency

## Slide 11: VLM2
Uses quad or ring vortices on surface
Uses horseshoe vortices on trailing edge to model wake
Biot-Savart has V~1/r^3 so difference in trailing vortices is typically minor

## Slide 12: 3D Panel Method
Sources and Doublets distributed evenly across each panel
Potential calculated at control points
  Boundary layer analysis
  Recalculation of potential at control points
Full field calculated with potential field

## Slide 13: 3D Panel Method
Advantages
Boundary Conditions
Takes into account wing thickness
Maps Cp over top and bottom
Von Nuemann
  Tangential flow condition
Dirichlet
  Potential inside body = Freestreem potential

## Slide 14: Created Wings Compared to Results in the Paper

## Slide 15: LLT Compared to VLM1 Results

## Slide 16: VLM2 Compared to VLM1

## Slide 17: 3D Panel Compared to VLM1

## Slide 18: Airfoil Shape

## Slide 19: Cp Distribution
3D Panel
VLM1

## Slide 20: Conclusions
VLM and 3D panel method yield different results
Due to the variable thickness, 3D Panel method may yield more accurate results
Potential flow models may be limited in flapping flight applications
Trends shown are repeatable

## Slide 21: Question?