## Slide 1: XFLR5 Methods and Their Application in “Constraints on the Wing Morphology of Pterosaurs”
By: Colin Parker

## Slide 2: Constraints on the wing morphology of pterosaurs
Wing shape is a mystery
  Few soft tissue fossils
No studies looking at the aerodynamic components
Want to combine biomechanical and aerodynamic constraints to predict shape
Notes: Motivation for study is to recreate wing formation
Fossil records only show hard tissue
Combine biological constraints with aerodynamic
Shown are some
  Straite
  Swept forward/back

## Slide 3: Longitudinal Stability Analysis
Notes: On aspect is longitudinal stability
Increase lift when ahead of center of mass pitch up
Pitch up increase lift more thus unstable
This paper tried to match Ac

## Slide 4: Aeroelastic Effects

## Slide 5: Effects of Washout
Notes: Aeroelastic effects
Plot lift coeffient with center of pressure location
%mac is typicllay taken as the distance from the leading edge of the MAC normalized by the MAC
Don’t have his MAC or MAC position
Applied lift behind the structural nuetral axis causes washout twist forward
t

## Slide 6: XFLR5
Notes: Wing geometries in XFLR5, show position chord offest dihedral and twist
Varied the twist distribution from 10 to -10(washout)
Cant see arrow on x but it points back

## Slide 7: Airfoil Shape

## Slide 8: LLT Lifting Line Theory
Kutta_Joukowski
Helmholtz Theorem
  The strength of a vortex filament is constant along its length
  A vortex filament cannot end in a fluid: must extend to infinity or form a closed path
Biot-Savart
Effective angle of attack
Repeat
Notes: Uses Xfoil data of CL vs AoA
Lifting line
Kutta relates lift to circulation
Biot-Savart relates circulation to downwash
Helmholtz shape horseshoe vortex

## Slide 9: LLT
Limitations
Does not account for sweep
Does not account for dihedral
Inviscid
Must have high Aspect Ratio
Notes: For this application not the best method
Does not account for sweep
High AR does not

## Slide 10: Lifting Surface Theory
Series of lifting lines
Circulation varies in both
  Span wise lifting line
  Chord wise vortices
Chord wise vortices extend into wake.
Biot-Savart
Flow tangency condition
Notes: Theory behind the vortex lattice method
Series of lifting line where circulation varies
Chordwise trailing vorticies vary in circulation as well
Apply biot savart
Apply flow tangency

## Slide 11: VLM Vortex Lattice Method
Assign circulation at control points
Biot-Savart Law
Flow tangency
Notes: Numerical approach
Easier to impleiment then solving
Apply circulation at control points

## Slide 12: VLM2
Uses quad or ring vortices on surface
Uses horseshoe vortices on trailing edge to model wake

## Slide 13: 3D Panel Method
Sources and Doublets distributed evenly across each panel
Potential calculated at control points
  Boundary layer analysis
  Recalculation of potential at control points
Full field calculated with potential field

## Slide 14: 3D Panel Method
Advantages
Boundary Conditions
Takes into account wing thickness
Maps Cp over top and bottom
Von Nuemann
  Tangential flow condition
Dirichlet
  Potential inside body = Freestreem potential

## Slide 15: Created Wings Compared to Results in the Paper
Notes: From Xcel spreedsheet of values that notes the foil shape
Email from colin/olivier saying
cannot find files but good to see trends match
Xcp for his wing move far in front of 0 hinting at a larger forward sweep

## Slide 16: LLT Compared to VLM1 Results

## Slide 17: VLM2 Compared to VLM1
Notes: Almost identical results VLM1 to VLM2

## Slide 18: 3D Panel Compared to VLM1
Notes: High angles of attach divernt results
3D panel accounts for variable thickness
When looking at pressure distribution gives more accurate picture

## Slide 19: Cp Distribution
3D Panel
VLM1

## Slide 20: Conclusions
VLM and 3D panel method yield different results
Due to the variable thickness, 3D Panel method may yield more accurate results
Potential flow models may be limited in flapping flight applications
Trends shown are repeatable

## Slide 21: Question?